## Slide 1: Microstrip patch antenna for breast cancer diagnosis With a frequency of 2.45 GHz and parameter sweep of the antenna dimensions
Candidates: Lecturer: Fabio Fanelli Prof. Marco Grande
Paolo Mazzone

## Slide 2: Reference paper «A microstrip patch antenna design for breast cancer detection»
Authors: R. Çalişkan, S. Gültekin, D. Uzer, Ö. Dündar
Whitepaper: Procedia - Social and Behavioral Sciences 195 — 2015
DOI: 10.1016/j.sbspro.2015.06.418

## Slide 3: Analysis purposes
The first objective of this work is to validate the main antenna design described in the paper;
Other antenna designs, discussed in the paper, will be analysed and compared in order to find the best to diagnose breast cancer;
To further improve the cancer detection, a parameter sweep will be performed. The patch dimensions will be changed to find the best parameters set;
Another parameter sweep will be performed to test the ability of the antenna to detect smaller cancerous masses.

## Slide 4: Antenna parameters
Name | Value [mm] | Description
sub_x | 65.4 | Substrate width
sub_y | 88.99 | Substrate length
sub_thick | 1.588 | Substrate thickness
p_x | 37.26 | Patch width
p_y | 28.83 | Patch length
inset_dist | 9.574 | Inset distance
inset_gap | 1.518 | Inset gap
f_length | 27.958 | Feed length
f_width | 3.036 | Feed width
g_thick | 0.035 | Ground thickness
b_thick | 80 | Normal breast tissue thickness/height
sk_thick | 1 | Skin tissue thickness
c_radius | 20 | Cancer sphere radius

## Slide 5: CST modeling of the patch antenna Antenna only, without the breast

## Slide 6: 3D representation of the antenna
Perspective view
Front view

## Slide 7: Scattering Parameters (S11)

## Slide 8: S11 – Antenna only

## Slide 9: VSWR (Voltage Standing-Wave Ratio)

## Slide 10: VSWR – Antenna only

## Slide 11: Directivity (3-dimensional pattern, Azimuthal plane, Elevation plane)

## Slide 12: Directivity – Antenna only
3-dimensional representation of the emissions of the antenna

## Slide 13: Directivity – Antenna only
Azimuth plane
Elevation plane

## Slide 14: Current distribution

## Slide 15: Current distribution – Antenna only
Phase: 90°
Maximum value: 54.8876 A/m
Phase: 180°
Maximum value: 54.8876 A/m

## Slide 16: Electric and Magnetic fields

## Slide 17: E/H Fields – Antenna only
E-field
Maximum value: 9595.06 V/m
H-field
Maximum value: 67.6191 A/m

## Slide 18: CST modeling of the patch antenna Antenna and breast without cancerous mass

## Slide 19: 3D representation of the antenna and the breast
Perspective view
Front view

## Slide 20: Dielectric and conductivity values of breast tissue
Tissue type | Dielectric (ε) | Conductivity (σ) [S/m] | Density [kg/m3]
Normal breast tissue | 9 | 0.4 | 978
Breast skin | 36 | 36.4 | 1020
Cancerous breast skin | 50 | 4 | 1100

## Slide 21: Scattering Parameters (S11)

## Slide 22: S11 – Antenna and breast

## Slide 23: VSWR (Voltage Standing-Wave Ratio)

## Slide 24: VSWR – Antenna and breast

## Slide 25: Directivity (3-dimensional pattern, Azimuthal plane, Elevation plane)

## Slide 26: Directivity – Antenna and breast
3-dimensional representation of the emissions of the antenna

## Slide 27: Directivity – Antenna and breast
Azimuth plane
Elevation plane

## Slide 28: Current distribution

## Slide 29: Current distribution – Antenna and breast
Phase: 90°
Maximum value: 30.1083 A/m
Phase: 180°
Maximum value: 30.1083 A/m

## Slide 30: Electric and Magnetic fields

## Slide 31: E/H Fields – Antenna and breast
E-field
Maximum value: 4136.98 V/m
H-field
Maximum value: 42.2117 A/m

## Slide 32: 1-Dimensional E/H-Fields
E-Field
H-Field

## Slide 33: CST modeling of the patch antenna Antenna and breast with cancerous mass

## Slide 34: 3D representation of antenna, breast, and cancer
Perspective view
Front view

## Slide 35: Scattering Parameters (S11)

## Slide 36: S11 – Antenna, breast, and cancer

## Slide 37: VSWR (Voltage Standing-Wave Ratio)

## Slide 38: VSWR – Antenna, breast, and cancer

## Slide 39: Directivity (3-dimensional pattern, Azimuthal plane, Elevation plane)

## Slide 40: Directivity – Antenna, breast, and cancer
3-dimensional representation of the emissions of the antenna

## Slide 41: Directivity – Antenna, breast, and cancer
Azimuth plane
Elevation plane

## Slide 42: Current distribution

## Slide 43: Current distribution – Antenna, breast, and cancer
Phase: 90°
Phase: 180°

## Slide 44: Electric and Magnetic fields

## Slide 45: E/H Fields – Antenna, breast, and cancer
E-field
Maximum value: 3944.59 V/m
H-field
Maximum value: 30.761 A/m

## Slide 46: 1-Dimensional E/H-Fields
E-Field
H-Field

## Slide 47: Comparison of the E-Field with and without cancer

## Slide 48: Comparison of the H-Field with and without cancer

## Slide 49: Parameter sweep Modified patch dimensions

## Slide 50: Parameter sweep details
Name | Set 1 | Set 2 | Set 3 | Set 4 | Set 5 | Set 6 | Set 7 | Set 8 | Set 9
p_x [mm] | 27.26 | 27.26 | 27.26 | 37.26 | 37.26 | 37.26 | 47.26 | 47.26 | 47.26
p_y [mm] | 18.83 | 28.83 | 38.83 | 18.83 | 28.83 | 38.83 | 18.83 | 28.83 | 38.83

## Slide 51: Comparison: S11 with and without cancer
S11 parameters – healthy tissue
S11 parameters – cancerous tissue

## Slide 52: Selecting the best parameters
Parameter set | Healthy tissue [dB] | Cancerous tissue [dB] | Difference [dB]
1 | -21.77 | -21.61 | -0.16
2 | -28.63 | -29.01 | 0.38
3 | -47.34 | -43.37 | -3.97
4 | -23.18 | -22.83 | -0.35
5 | -30.28 | -30.56 | 0.28
6 | -41.66 | -39.55 | -2.11
7 | -24.07 | -23.89 | -0.18
8 | -31.44 | -32.26 | 0.82
9 | -38.21 | -36.69 | -1.52

## Slide 53: Other antenna designs

## Slide 54: 1st alternative design: modified ground plane
Perspective view
Default parameters
Back view
Default parameters

## Slide 55: 1st alternative design: modified ground plane
S11 parameters – healthy breast
Default parameters
S11 parameters – cancerous breast
Default parameters
Difference: 0.46 dB

## Slide 56: 1st alternative design: modified ground plane
Perspective view
Optimized parameters
Back view
Optimized parameters

## Slide 57: 1st alternative design: modified ground plane
S11 parameters – healthy breast
Optimized parameters
S11 parameters – cancerous breast
Optimized parameters
Difference: [1] 4.69 dB, [2] 3.99 dB

## Slide 58: 2nd alternative design: big slot, modified ground
Perspective view
Default parameters
Front view
Default parameters

## Slide 59: 2nd alternative design: big slot, modified ground
S11 parameters – healthy breast
Default parameters
S11 parameters – cancerous breast
Default parameters
Difference: 0.44 dB

## Slide 60: 2nd alternative design: big slot, modified ground
Perspective view
Optimized parameters
Front view
Optimized parameters

## Slide 61: 2nd alternative design: big slot, modified ground
S11 parameters – healthy breast
Optimized parameters
S11 parameters – cancerous breast
Optimized parameters
Difference: 5.32 dB

## Slide 62: 3rd alternative design: thin slot, modified ground
Perspective view
Default parameters
Front view
Default parameters

## Slide 63: 3rd alternative design: thin slot, modified ground
S11 parameters – healthy breast
Default parameters
S11 parameters – cancerous breast
Default parameters
Difference: 0.59 dB

## Slide 64: 3rd alternative design: thin slot, modified ground
Perspective view
Optimized parameters
Front view
Optimized parameters

## Slide 65: 3rd alternative design: thin slot, modified ground
S11 parameters – healthy breast
Optimized parameters
S11 parameters – cancerous breast
Optimized parameters
Difference: 4.92 dB

## Slide 66: Parameter sweep Modified cancer radius

## Slide 67: Parameter sweep details
Name | Set 1 | Set 2 | Set 3 | Set 4 | Set 5 | Set 6 | Set 7 | Set 8 | Set 9 | Set 10 | Set 11
c_radius [mm] | 0.2 | 2 | 3.03 | 5.86 | 8 | 8.68 | 11.51 | 14 | 14.34 | 17.17 | 20

## Slide 68: S11 parameters
Entire plot
Zoom – Detailed view

## Slide 69: SAR (Specific Absorption Rate)

## Slide 70: SAR – Healthy tissue
SAR – 3D view
SAR – Back view
Maximum value: 33.57 W/kg; Total value: 0.95 W/kg

## Slide 71: SAR – Cancerous tissue (20 mm)
SAR – 3D view
SAR – Back view
Maximum value: 33.33 W/kg; Total value: 0.66 W/kg

## Slide 72: SAR – Cancerous tissue (2 mm)
SAR – 3D view
SAR – Back view
Maximum value: 33.47 W/kg; Total value: 0.67 W/kg

## Slide 73: Conclusions

## Slide 74: Obtained results
There is a certain difference between the E-fields or S-parameters in the healthy tissue compared to the cancerous tissue;
The difference observed is highlighted when the antenna dimensions are varied; the best parameters set is the third, where the patch is slightly higher than the original one;
By comparing the differences between the biggest dips in the S-parameters plots, the paper affirmed that the best antenna design was the one with a thin slot. This has been proven true, but only using the default parameters (difference of 0.59 dB): by using the optimized ones, the best design is the one with the big slot, which provides a significant increase in the difference (5.32 dB).

## Slide 75: Obtained results
The best antenna design can detect a cancer sphere with a radius up to 0.2 mm;
The same antenna is safe to use, because its maximum total SAR is 0.95 W/kg.